## Slide 1: ARIADNE:
A General Purpose
Indoor Navigation System
Developed by undergraduate students
from the National Technical University of Athens
HiPEAC Student Challenge – 21/01/2025

## Slide 2
ARIADNE System Architecture
ARIADNE - NTUA
1

## Slide 3
What are beacons?
Why use beacons?
Which beacons?
Bluetooth beacons
compact devices
periodical signal transmission
reaching nearby devices
RSSI for location estimation
BLE support
continuous operation on a single battery for extended time
Nordic Semiconductors nRF52840 SoC
fine-tuned control over range and energy consumption
ARIADNE - NTUA
2

## Slide 4
Classic beacon VS ARIADNE beacon
Advertising packets every 100ms
continuous operation
no logic needed
receiving packets from devices
logic to decide whether to advertise packets or enter sleep mode
ARIADNE - NTUA
3

## Slide 5
ARIADNE beacon details
Advertising
Observing
Interrupting
Sleeping
ARIADNE - NTUA
BLE signal transmission
100ms interval
same as “classic” beacon
continuously receiving signals
interval < 1s
filters out unwanted packets
utilization of Timer
when packets are received
interrupt every 2s
when receiving 0 packets
no advertising
dynamically changing duration
4

## Slide 6
ARIADNE - NTUA
supply voltage 3.8V
observation interval =
scan window + waiting duration
min. current used on sleep mode
max. current used when receiving
packets for consecutive time periods
average current : 3.85mA
Power Efficiency
5

## Slide 7
Localization Algorithm
Simple Trilateration
Least Squares method
RSSI : Received Signal Strength Indicator
Measured Power : factory-calibrated constant
N : obstacle density of building
ARIADNE - NTUA
6

## Slide 8
Floor Plan Analysis
Detect the walkable space and construct a navigation graph
ARIADNE - NTUA
Important Components
Doors
YOLO11 CNN
Walls/
Obstacles
Computer Vision
Rooms
YOLOv8 CNN
7

## Slide 9
Door Detection
Use of YOLO11 CNN model with bounding box detection
ARIADNE - NTUA
8

## Slide 10
Room Detection
Use of YOLOv8 CNN model with instance segmentation
9

## Slide 11
Wall Detection
Simple door bounding box removal may result in information loss
After removing the doors we find the contours of the binary image to detect walls and obstacles
ARIADNE - NTUA
Solution: Use multi-otsu thresholding to only remove doors
10

## Slide 12
Graph Construction
Nodes: 10,000+
Edges: 70,000+
Nodes: 500
Edges: 1,800
ARIADNE - NTUA
11

## Slide 13
ARIADNE System Demo
ARIADNE - NTUA
12

## Slide 14
ARIADNE Mobile Application Demo
ARIADNE - NTUA
13

## Slide 15
ARIADNE - NTUA
Thank you for your attention!
Athanasios Tsoukleidis-Karydakis
Dimitrios-David Gerokonstantis Dionisios Rafail Defteraios Epimenidis Kountourakis
Filippos Sevastakis Konstantinos Ioannou Maria Zerva Savvina Nastou Spyros Papadopoulos